## Slide 1: Brain Tumor Segmentation Using Deep Learning
Machine learning II
Tornike Jikhvashvili

## Slide 2
Problem Definition
What is Brain Tumor Segmentation?
Automatically identifying and outlining tumor regions in brain MRI scans.
Converting medical images into precise pixel-level tumor masks
Why is it Challenging?
Irregular tumor shapes - no standard size or boundary patterns
Variable intensities - tumors appear differently across MRI modalities
Complex anatomy - tumors can be in different brain regions

## Slide 3: Motivation
Clinical impact
700,000+ new brain tumor cases each year
Early detection is critical for treatment success and patient survival
Time-sensitive diagnosis - delays can worsen patient outcomes
Limitations
Manual segmentation takes 3-4 hours per patient
Radiologist fatigue leads to inconsistent results
Limited availability of expert neuroradiologists
Subjective interpretation
Benefits of automation
Speed
Consistency
Scalability
Objectivity
Earlier treatment

## Slide 4: Dataset - BraTS 2020
Brain Tumor Segmentation Challenge
International benchmark dataset for brain tumor segmentation
369 multi-institutional cases with expert annotations
High-grade glioma patients - most aggressive brain tumor type
Multi-Modal MRI Data
T1: Native T1-weighted - shows brain anatomy
T1ce: T1-weighted with contrast enhancement - highlights active tumor
T2: T2-weighted - shows tumor and surrounding edema
FLAIR: Fluid-attenuated inversion recovery - suppresses healthy tissue signal
Ground Truth Labels
Expert annotations by neuroradiologists
Pixel-level segmentation masks
Original multi-class labels: enhancing tumor, tumor core, whole tumor, healthy tissue
Data Characteristics
Image size: 240×240×155 voxels per modality
Standardized preprocessing - skull-stripped, co-registered
High quality medical-grade imaging data

## Slide 5: Methodology Overview
2D Slice-Based Approach
Converting 3D volumes to 2D slices for training and inference
Slices processed independently rather than full 3D volume
Binary vs. Multi-Class Segmentation
Original BraTS: 4-class segmentation (enhancing tumor, tumor core, whole tumor, background)
My approach: Binary classification (tumor vs. background)
Data Augmentation
Random Rotation, Random Flipping, Random Brightness and Contrast Adjustment
Normalization
min-max normalization to scale the pixel values to a 0-1 range
Optimizers: Adam, AdamW, SGD
Loss: Dice+BCE
LR: 0.0005, 0.005
Epoch: 50
Batch size: 6

## Slide 6: Models that I used
U-Net | Res-U-Net
Core Idea: Standard Encoder-Decoder with long-range skip connections. | Core Idea: Standard U-Net with Residual Blocks for better gradient flow.
Key Components | 
A "downsampling path" that extracts high-level features. | R- A "downsampling path" that extracts high-level features
An "upsampling path" that reconstructs the segmentation mask. | - An "upsampling path" that reconstructs the segmentation mask.
"Skip connections" that merge features from the downsampling path directly to the upsampling path. | Residual (or shortcut) connections within the convolutional blocks.

## Slide 7
Chart: Dice Score
| U-net | Res-Unet
Train | 0.8773 | 0.8725
Test | 0.8455 | 0.8641

## Slide 10
Potential improvements
Transition to 3D segmentation
Multi-class segmentation
More advance architectures